## Slide 1: Lights Out Management

## Slide 2: Intelligent Platform Management Interface (IPMI)
Remote management and monitoring
Hardware level
  Works with machine powered down
Message based

## Slide 3: IPMI Features
System Monitoring
  System temperatures
  Voltages
  Fans
  Power Supplies
  Chassis Intrusion
System controls
  Power on/off
  rebooting
  watchdog timer controls
Consoles
  Serial interface
  KVM over IP

## Slide 4: IPMI Why?
You can watch the administer boot processes remotely
  Before SSH is available
  Make changes in BIOS remotely
Power cycling of machine remotely
System monitoring
  Crude but powerful

## Slide 5: IPMI Interface Types
Serial
  not common, but standard allows for it
Out-of-Band
  requires a second ethernet connection
  Fast enough for video
Side-Band
  Shared ethernet connection
  Reduced throughput
  Fast enough for serial console, but not video

## Slide 6: IPMI Services
Services only required to run on local machine
Running ipmitool on local machine requires root
Service name | ipmi; ipmievd
Packages | OpenIPMI; ipmitool
Related Commands | ipmitool

## Slide 7: IPMI Module Loading
lsmod
  View loaded kernel modules
modprobe [module_name]
  Load kernel module
/etc/rc.modules
  Load kernel module at boot