## Slide 2: Ceph: An Open Source Object Store
Evan Harvey
Gustavo Rayos
Nick Schuchhardt
Mentors: David Bonnie, Chris Hoffman, Dominic Manno

## Slide 3
What is an Object Store?
Manages data as objects
Offers capabilities that are not supported by other storage systems
Object Storage vs. Traditional Storage

## Slide 4
What is Ceph?
An object store and filesystem
Open source and freely available
Scalable to the Exabyte level

## Slide 5
Basic Ceph Cluster
Monitor Node
  Monitors the health of the Ceph cluster
OSD Node
  Runs multiple Object Storage Daemons (One daemon per hard drive)
Proxy Node
  Provides an object storage interface
  Can interact with cluster using PUT/GET operations
  Provides applications with a RESTful gateway to the Ceph storage cluster

## Slide 6
Basic Ceph Cluster

## Slide 7
But Why?
Campaign Storage
More reliable than other file systems
POSIX compliant
Scales better than RAID
Cost efficient

## Slide 8
Project Goals
Build a Ceph storage cluster
  1 Monitor node
  6 OSD nodes (Around 20 OSD daemons each)
  3 proxy nodes
Erasure coding profiles
Single vs. Multiple proxies

## Slide 9
Test Environment
CentOS 6.6
Ten HP ProLiant D380P Gen8 Servers
Three Supermicro 847jbod-14 (45 disks each)
Mellanox Infiniband 56 Gb/s
Two SAS cards 6 Gb/s
  8 ports at 600 MB/s
Four Raid cards 6 Gb/s
  8 PCI Express 3.0 lanes

## Slide 10
Our Set Up

## Slide 11
Pools and PGs

## Slide 12
Pools and Placement Groups
  An object belongs to a single placement group
  Pools group placement groups
  Placement groups belong to multiple OSDs

## Slide 13
CRUSH!
12
Controlled Replication Under Scalable Hashing (CRUSH)
Algorithm finds optimal location to store objects
Stripes objects across storage devices
On the OSDs

## Slide 19
Erasure Coding
High resiliency to data loss
Smaller storage footprint than RAID
Data is broken up into object chunks
Striped across many hard drives
K + M values used to stripe
Various erasure profiles

## Slide 20
Erasure Coding

## Slide 21
Results
Difficult to install and configure Ceph on CentOS 6.6
Multiple proxies write faster than a single proxy
Replicated profile was faster than the erasure coded profiles
K + M values did not significantly affect read and write speeds

## Slide 25
Ceph Headaches
Documentation is inaccurate
Nodes must be configured in specific order
  Monitor  OSDs  Proxies
Ceph was unable to recover after hardware failure
Could only use one out of the four Infiniband lanes
Unable to read in parallel

## Slide 26
Conclusion
Ceph is difficult to install and configure
Stability of Ceph needs to be improved
Unable to recover from hardware failures during benchmarking
Performance was promising

## Slide 27
Future Work
Investigate bottleneck of tests
Further explore pool configurations and PG numbers
Look into Ceph monitoring solutions
Test differences between ZFS/BTRFS vs XFS/EXT4

## Slide 28
Acknowledgements
Mentors: David Bonnie, Chris Hoffman, Dominic Manno
Instructors: Matthew Broomfield, assisted by Jarrett Crews
Administrative Staff: Carolyn Connor, Gary Grider, Josephine Olivas, Andree Jacobson

## Slide 29
Questions?
28
Objects stores?
Ceph and our object store?
Installation and configuration?
Pools and Placement groups?
CRUSH?
Erasure coding?
K + M?